## Slide 1
Rasp
berry
pi

## Slide 2: Models
Raspberry pi 1 Model B+
Raspberry pi 2 model B
Raspberry pi 3 model B+
Raspberry pi zero
Raspberry pi 3 model B
Raspberry pi zero W

## Slide 3: Raspberry pi 3 [specifications]
Quad Core 1.2GHz Broadcom BCM2837 64bit CPU
1GB RAM
BCM43438 wireless LAN and Bluetooth Low Energy on Board
40 – pin extended GPIO
4 USB 2 ports
4 pole stereo output and composite video port

## Slide 4: Specifications continued..
Full size HDMI
CSI camera port for connecting a Raspberry pi camera
DSI display port for connecting a raspberry pi touchscreen display
Micro SD port for loading your operating system and storing data
Micro SD port for Upgraded switched Micro USB power source up to 2.5A

## Slide 5: Raspberry pi 3 [pinout]

## Slide 6: Raspberry pi zero W [specifications]
802.11 b/g/n wireless LAN
Bluetooth 4.1
Bluetooth Low Energy (BLE)
1GHz, single-core CPU
512MB RAM

## Slide 7: Raspberry pi zero W[specifications]
Mini HDMI and USB On-The-Go ports
Micro USB power
HAT-compatible 40-pin header
Composite video and reset headers
CSI camera connector

## Slide 8: Practical session[Controlling the pi from a web server]
Prerequisites
A breadboard
Raspberry pi
Jumper wires
2 resistors
2 LED’s
A power source

## Slide 9: Knowledge check
Understanding what a block of code would mean (python)
GPIO pins
Sensor integration

## Slide 10: Process [connections]
Working with the pi zero [connections]
Working with the pi3

## Slide 11: Process [software]
Virtual environments
sudo pip install virtualenv virtualenvwrapper
sudo rm –rf ~/.cache/pip
export WORKON_HOME=$HOME/.virtualenvs
source /usr/local/bin/virtualenvwrapper.sh

## Slide 12: Virtual environments cont..
echo -e "\n# virtualenv and virtualenvwrapper" >> ~/.profile
echo "export WORKON_HOME=$HOME/.virtualenvs" >> ~/.profile
echo "source /usr/local/bin/virtualenvwrapper.sh" >> ~/.profile
source ~/.profile
mkvirtualenv cv -p python2

## Slide 13: Flask
Sudo apt-get install python-pip python-flask
Sudo pip-install flask

## Slide 14: Organization
----python code ---
mkdir [name]
cd [name]
Sudo nano [filename]
---- web server -----
Mkdir templates
Cd templates
Sudo nano [filename2]

## Slide 15: Test
Cd ..
Sudo python name.py

## Slide 16: On your web browser
http://IPADDRESS

## Slide 17: Applications
Automatic actuation – the case of automatic irrigation

## Slide 18: Questions & Comments